Fully quantum description of a three level
maser, driven by a thermal bath
Sander Stammbach
Prof. Dr. Patrick Potts
Dr. Mateo Brunelli
Marcelo Janovitch
7.3.2023
[Speaker Notes: Hallo]

---
Contents
Theory
3-level-system
Master equation
Lasing transition
PHAV state
Double threshold
Thermodynamics
Heat current
Entropy production
Conclusion
[Speaker Notes: First we look at the theory and the model of a three level maser]

---
Introduction
http://web.mit.edu/jianshucaogroup/quther2015.html
Heat engine
Three-level maser
Scovil and Schulz-DuBois(1959)
Absorbtion , spontaneous and stimulated emission
[Speaker Notes: One of the most important question… steam gas quantum system convert heat into a driven field insteaf of a moving piston. in this project three level system drven by bath Important ground work Einstein based 1959 scovil schulz groundwork In their thermodynamic analysis, they used a single-atom laser.]

---
3-level-maser
Schematic representation of a three-level maser heat engine continuously coupled to two reservoirs of temperatures $T_h$; and $T_c$. The three energy levels are described by $E_1,E_2,E_3$. The system is interacting with a quantized single mode field. $\lambda$ represents the strength of matter-field coupling. The $\omega_h, \omega_c, \omega_{cav}$ describes the transition frequencies.
Schematic representation of a three-level maser heat engine two reservoirs of temperatures $T_h$; and $T_c$. energy levels $E_1,E_2,E_3$. Is interacting with a quantized single mode field. $\lambda$ . The transition frequencies $\omega_h, \omega_c, \omega_{cav}$ .
\begin{equation} H=H_{free}+H_{int} \end{equation} \begin{equation} H_{free}=\sum_{i=1}^3 \hbar \omega_i \ket{i}\bra{i}+\hbar \omega_f a^{\dag}a, \end{equation} \begin{equation} H_{int}=\hbar g(\sigma_{12}a^{\dag}+\sigma_{21}a). \end{equation}
[Speaker Notes: A maser consist 2 elements gain medium is a transition between atomic states decay from higher to lower, photon is created. Population inversion on E2 Explain the image one direction cyrcle Cavity with small leaking kappa w=E2-E1/h in this work wcav = wf therfore resonace]

---
Master equation
An arbitary state of a cavity and an atom can be described by the total density operator ${\rho}(t)$ . This density operator can bederrived by the the Lindblad-master-equation.\\ \begin{equation} \dot{\rho}(t)=\frac{1}{i \hbar}[H,\rho]+ \mathcal{L}_{h}\rho+ \mathcal{L}_{c}\rho+ \mathcal{L}_{cav}\rho.\ \end{equation}\\
The hole calculations are made for steady-states, therefore no time dependency=>
$\dot{\rho}(t)=0$
[Speaker Notes: An arbitry state can described by rho rho is given by diff von neuman, unitary part reversible Dissipative part Calculations are done with steady states]

---
3-Level maser Hamiltonian
\begin{equation} H=H_{free}+H_{int} \end{equation} The total Hamiltonian consistof two parts. The part of the photons is, which describes the photons in the cavity: \begin{equation} H_{free}=\sum_{i=1}^3 \hbar \omega_i \ket{i}\bra{i}+\hbar \omega_f a^{\dag}a, \end{equation} And the interaction Hamiltonian or Jaynes-Cummings Hamiltonian: \begin{equation} H_{int}=\hbar g(\sigma_{12}a^{\dag}+\sigma_{21}a). \end{equation} The coupling constants $g$ strong for the Hamiltonian and the $\kappa$ for the Liouvillian part. The coupling constant $g$ is given by $\frac{\Omega}{\hbar}$.
[Speaker Notes: Hamilton is the energy operator Explain the hamiltons transiton operators frequencies and coupling constant The hole conclusion is made for steady states]

---
Master equation
\begin{equation} \dot{\rho}(t)=\frac{1}{i \hbar}[H,\rho]+\underbrace{\mathcal{L}_{h}\rho+ \mathcal{L}_{c}\rho+ \mathcal{L}_{cav}\rho}_{\mathcal{L}\rho}.\ \end{equation}\\ The Liouvillian is\\ \begin{equation} \begin{aligned} \mathcal{L}\hat{\rho}=\textcolor{red}{\frac{\gamma_h}{2}(n(\omega_h,T_h)+1) \cdot \mathcal{D}[\sigma_{13}]\rho +\frac{\gamma_h}{2}n(\omega_h,T_h)\cdot \mathcal{D}[\sigma_{31}]\rho} \\ \textcolor{blue}{+\frac{\gamma_c}{2}(n(\omega_c,T_c)+1)\cdot \mathcal{D}[\sigma_{23}]\rho +\frac{\gamma_c}{2}n(\omega_c,T_c) \cdot \mathcal{D}[\sigma_{32}]\rho} \\ +\kappa(n(\omega_f,T_f)+1) \cdot\mathcal{D}[a]\rho+ \kappa n(\omega_f,T_f)\cdot \mathcal{D}[a^{\dag}]\rho. \end{aligned} \end{equation} Where $\sigma_{ij}=\ket{i}\bra{j}$.\\ $a $ is the ladder operator.\\ $\gamma = 1$ are the decay rates $\mathcal{D}$ is defined with following formula: \begin{equation} \mathcal{D}[A]\rho=(2A \rho A^{\dag}-A^{\dag}A\rho-\rho A^{\dag}A), \end{equation}
[Speaker Notes: The interactions with the baths described by the liouvillion superoperators Describe coupling with hot bath… Cold… Photons... transition op bose-einstein occupation number gamma are decay rates =1 in thermes of gamma]

---
PHAV State
$\ket{\alpha}=e^{\frac{-|\alpha|^2}{2}}\sum_{n=0}^{\infty}\frac{|\alpha|^n e^{in\phi}}{\sqrt{n!}} \ket{n}$
$\rho_{PHAV}=\int_0 ^{2\pi}\frac{d\phi}{2\pi}\ket{\alpha(\phi)}\bra{\alpha(\phi)}=\sum_{n=0}^{\infty}p_{nn}\ket{n}\bra{n}$
\begin{equation} \rho_{PHAV}= \sum_{n=0}^{\infty}\exp(-|\alpha|^2)\frac{|\alpha|^{2n}}{n!} \ket{n}\bra{n}.\label{11} \end{equation}
[Speaker Notes: For a laser we expect Coherent light smaephase same frequency described by coherent state poisson distribution But in this phase-averaged coherent state (PHAV) averaged phase ϕ around 2π. Randomizing doesnt photon-number distribution]

---
PHAV State
Wigner function and phase-averaged coherent states
$\ket{\alpha}=e^{\frac{-|\alpha|^2}{2}}\sum_{n=0}^{\infty}\frac{|\alpha|^n e^{in\phi}}{\sqrt{n!}} \ket{n}$
Two ilustrations of a PHAV -state is done in qutip.
\begin{equation} \rho_{PHAV}= \sum_{n=0}^{\infty}\exp(-|\alpha|^2)\frac{|\alpha|^{2n}}{n!} \ket{n}\bra{n}.\label{11} \end{equation}
[Speaker Notes: . In order to bettter describe A Wigner function is a representation of a general quantum state of light [1]. The function describes the probability density in phase space.]

---
Double threshold behaviour
In Fig b) we see, that the lasing have a clear peak.
\langle Pi \rangle = Tr[\ket{i}\bra{i} \rho]
Sheng Wen Li et al. “Quantum statistics of a single-atom Scovil-Schulz-DuBois heatengine”
[Speaker Notes: When we work with density ...comon Tr[A*rho] expectation value The occupatioin probability is seen by take (T r[|i⟩ ⟨i| ρ]), i stands… If P 2 > P 1 we get popu…..it is nesesary for lasing, stimulated emmision. ploting Tr[nρ] vs photonumber give special courve increase n_h implicatet a increasing temperature. Photonumber Increase up to a peak and decrease again. Call it double threshold behaviour Explanaten: This double threshold behaviour can can be explained by the Zeno Effect. The Zeno effect describes that the transition from one state to the other can be stopped by rapid successive measurements. The system behaves similarly when sufficient stimulation is applied quickly.]

---
Double threshold behaviour
For all of the four the parameters are $n_c=0.001 n_f=0.02,\kappa=0.1\gamma_h$. Cavity with a small leaking. \textbf{a)}The parameters for $n_h$is $n_h=0.2 $. \textbf{b)}$ n_h=2.6$ \textbf{c)} $ n_h=5.5$ \textbf{d)}$ n_h=20$.
[Speaker Notes: this double threshold by looking on the wigner-Fockplots First clously to a vacum stat Parameters are all the same just nh increase]

---
Heat currents
\langle J_{tot}\rangle=Tr[H_{free}\cdot \mathcal{L}_h[\rho]]+Tr[H_{free}\cdot \mathcal{L}_c[\rho]]+Tr[H_{free}\cdot \mathcal{L}_{cav}[\rho]]=0
\Delta U=\Delta Q+\Delta W = 0 =>
[Speaker Notes: The first law of Thermodynamics says: ”The change in internal energy of a closed system is equal to the sum of the change in heat and the change in work.” That is equal to the equation .. In the case of this calculation with steady states ∆U or d⟨H⟩ is zero. ∆W is also zero. This can be justified because ∂t H = 0 and therefore the the first law says that ⟨Jtot ⟩ have to be zero. Tr[H*L rho] vs g]

---
Entropy production
\\ Entropy:\\ $\Delta S = \sigma-\frac{Q}{T}$ \\ Second law:\\ $\dot{\sigma} \geq 0 $\\ Entropy production rate:\\ $\dot{\sigma} =\frac{J_c}{T(n_c)}+\frac{J_h}{T(n_h)}+\frac{J_{cav}}{T(n_{cav})}$
[Speaker Notes: the second law of thermodynamics says that, for a isolated system, the entropy always remains the same or increases, but never becomes smaller. In terms of instantaneous quantities, this principle can be expressed by the entropy production rate σ̇, which should always be larger or equal than zero. Entropy production rate calulate by heat current dividet by the temperature The entropy production rate is an important quantitative measure of a non-equilibrium process and knowing its value is indicative of useful information about the system such as heat dissipated,, efficiency (if the non-equilibrium system in question is an engine,) as well as free energy differences]

---
Entropy production
\\ Entropy:\\ $\Delta S = \sigma-\frac{Q}{T}$ \\ Second law:\\ $\dot{\sigma} \geq 0 $\\ Entropy production rate:\\ $\dot{\sigma} =\frac{J_c}{T(n_c)}+\frac{J_h}{T(n_h)}+\frac{J_{cav}}{T(n_{cav})}$
[Speaker Notes: plot ofexpectation value of the photon number versus nh is simular to the entropyprduction rate. We see also a double threshold behaviour. If nh is large, the coupling with the hot bath dominates with respect to the coupling to the cold bath and to the photons leaking outside the cavity. The larger nh , the closer the system gets to be an equilibrium state with the hot bath]

---
Contents
Verified states which look simular to PHAV state!
Double threshold behaviour in entropy production and photon number!
If we increase the temperature from
the hot bath, we see that the occupation probability of P 2 increase as well.
In future look for the TUR
https://link.
aps.org/doi/10.1103/PhysRevLett.2.262.

---
Questions?
$\ket{\alpha}=e^{\frac{-|\alpha|}{2}}\sum_{n=0}^{\infty}\frac{|\alpha|^n e^{in\phi}}{\sqrt{n!}} \ket{n}$
$ \begin{aligned} \mathcal{L}\hat{\rho}=\frac{\gamma_h}{2}(n(\omega_h,T_h)+1) \cdot \mathcal{D}[\sigma_{13}]\rho +\frac{\gamma_h}{2}n(\omega_h,T_h)\cdot \mathcal{D}[\sigma_{31}]\rho \\ +\frac{\gamma_c}{2}(n(\omega_c,T_c)+1)\cdot \mathcal{D}[\sigma_{23}]\rho +\frac{\gamma_c}{2}n(\omega_c,T_c) \cdot \mathcal{D}[\sigma_{32}]\rho \\ +\kappa((\omega_f,T_f)+1) \cdot\mathcal{D}[a]\rho+ \kappa n(\omega_f,T_f)\cdot \mathcal{D}[a^{\dag}]\rho. \end{aligned} $
w(z)=2 \exp\bigl[-2\bigl(|\alpha|^2+|z|^2\bigr)\bigr) I_0 (4|\alpha| |z|).