Fully quantum description of a tree level
maser, driven by a thermal bath
Sander Stammbach
Prof. Patrick Plotts
12 November 2022

---
Contents
Theory
3-level-system
Master equation
Lasing transition
PHAV state
Doublethreshold
Thermodynamics
Heat current
Entropy production
Conclusion

---
3-level-maser
Schematic representation of a three-level maser heat engine contin-
uously coupled to two reservoirs of temperatures Th and Tc having coupling
constants Γh and Γc , respectively. The system is interacting with a classical
single mode field. λ represents the strength of matter-field coupling

---
3-Level maser Hamiltons
\begin{equation} H=H_{free}+H_{int} \end{equation} The total Hamiltonian consistof two parts. The part of the photons is, which describes the photons in the cavity: \begin{equation} H_{free}=\sum_{i=1}^3 \hbar \omega_i \ket{i}\bra{i}+\hbar \omega_f a^{\dag}a, \end{equation} And the interaction Hamiltonian or Jaynes-Cummings Hamiltonian: \begin{equation} H_{int}=\hbar g(\sigma_{12}a^{\dag}+\sigma_{21}a). \end{equation} The coupling constants $g$ strong for the Hamiltonian and the $\kappa$ for the Liouvillian part. The coupling constant $g$ is given by $\frac{\Omega}{\hbar}$.

---
Master equation
The master equation:\\ \begin{equation} \dot{\rho}(t)=\frac{1}{i \hbar}[H,\rho]+ \mathcal{L}_{h}\rho+ \mathcal{L}_{c}\rho+ \mathcal{L}_{cav}\rho.\ \end{equation}\\ The Liouvillian is:\\ \begin{equation} \begin{aligned} \mathcal{L}\hat{\rho}=\frac{\gamma_h}{2}(n(\omega_h,T_h)+1) \cdot \mathcal{D}[\sigma_{13}]\rho +\frac{\gamma_h}{2}n(\omega_h,T_h)\cdot \mathcal{D}[\sigma_{31}]\rho \\ +\frac{\gamma_c}{2}(n(\omega_c,T_c)+1)\cdot \mathcal{D}[\sigma_{23}]\rho +\frac{\gamma_c}{2}n(\omega_c,T_c) \cdot \mathcal{D}[\sigma_{32}]\rho \\ +\kappa((\omega_f,T_f)+1) \cdot\mathcal{D}[a]\rho+ \kappa n(\omega_f,T_f)\cdot \mathcal{D}[a^{\dag}]\rho. \end{aligned} \end{equation} The $\sigma_{12} $ is the transition operator and defined as $ \ket{1}\bra{2}$.\\ Similar for $\sigma_{13}=\ket{1}\bra{3}, \sigma_{23}=\ket{2}\bra{3}=a$ . It describe the transition between a atomic state $a$ to $b$. $\mathcal{D}$ is defined with following formula: \begin{equation} \mathcal{D}[A]\rho=(2A \rho A^{\dag}-A^{\dag}A\rho-\rho A^{\dag}A), \end{equation}

---
PHAV State
\begin{equation} W(z)=2 \exp\bigl[-2\bigl(|\alpha|^2+|z|^2\bigr)\bigr) I_0 (4|\alpha| |z|). \end{equation}

---
Contents

---
Contents